## Slide 1: Lab2: Multiply Accumulation Unit Design with SystemC
Machine Learning Intelligent Chip Design
2024 Spring

## Slide 2: Introduction
Design a multiply accumulate unit
  𝑌=𝐴×𝐵+𝐶

## Slide 3: Environmental preparation
cp /RAID2/COURSE/mlchip/mlchipTA01/sharing/lab2.zip .
unzip lab2.zip
source /RAID2/cad/synopsys/CIC/pa_virtualizer.cshrc
pct &

## Slide 4: SystemC
Source file
  xxx.h
  xxx.cpp
  Main.cpp
Makefile
  Compile the source file

## Slide 5: SystemC
Edit your source code by editor (e.g., notepad++,…)
  MAC.h

## Slide 6: SystemC
Edit your source code by editor (e.g., notepad++,…)
  MAC.h

## Slide 7: Build & Run
cd < file path >
%make

## Slide 8: Platform Architect
Create project -> Project name -> Project file name -> OK

## Slide 9: Platform Architect
Import SystemC Modules -> Add

## Slide 10: Platform Architect
Choose the source file -> OK

## Slide 11: Platform Architect
Hardware block
IP Library

## Slide 12: Platform Architect

## Slide 13: Platform Architect
Change protocol of clock port
Double click Clock -> Click Default -> Choose CLOCK

## Slide 14: Platform Architect
Repeat the same action to change the clock protocol of Pattern and Monitor block

## Slide 15: Platform Architect
Create the block
  Click and drag to the design window

## Slide 16: Platform Architect
Use connection tool to connect the block

## Slide 17: Platform Architect
Click Clock block -> Set clock period
  division -> 5
  cycle -> 40

## Slide 18: Platform Architect
Click Reset block -> Set reset period
  _ticks -> 10

## Slide 19: Platform Architect
Console
  Show the simulation result

## Slide 20: Lab Requirement
Complete MAC unit.
  Use Platform Architecture to simulate output result.
  Upload screenshots of simulation results and module connection to E3@NYCU